## Slide 1
3.5”
30”
29”
36”
3 3/16”
18”
7.5”
All measurements based on 2x10 (1-½” thick) wood
- a standard 1x10 is too thin (really only ¾” thick)
To make the seat height 18”, the legs should be cut to 18-½”
- 10 degree slope plus the angle you cut off at the top and bottom
Cross brace is a standard 2x4, with the tenons ¼” narrower on each side and ½” top and bottom as indicated in the drawing
Brace peg is best made from 1” dowel
- 1 brace peg on the inside forces legs out making them always tight
Only need 1 brace peg, but on the inside
See tenon details on next page
10o
Terafan Greydragon’s Bench design
2-1/2”
2-3/4”
3-1/4”

## Slide 2
Terafan Greydragon’s Bench design – page 2
3 3/16”
9-½”
2”
1-½”
9-1/2”
The “extra” dashed lines are an attempt to
show the results of the 10o angle.
The holes must be cut with the
10o angle taken in account.
The top and bottom of the legs must
have the 10o angle taken in account.
2.5”
2”
2”
36”
Bench top
1” round hole (to fit the peg) with the center 3” in from end
Detail on the peg hole in the tenon
Best to drill hole prior to cutting top/bottom/sides off to make tenon
1-½”
2-½”
1-½”
3-1/4”
3”
9-1/2”
2-1/2”